## Slide 1: TECHNOVATION 2K26
TITLE PAGE
Project Title - Safe Charging Chip for Mobile Phones
Theme - Battery and Charging Safety
Category - Hardware (Embedded + FPGA)
Team Name - LogicNova
Notes: Title page. Project: Safe Charging Chip for Mobile Phones. Team LogicNova at Technovation 2k26.

## Slide 2: SAFE CHARGING CHIP An independent hardware safety layer for phone charging
FROM: UNPROTECTED CHARGING
No temperature awareness
One protection layer inside the phone
The user cannot verify it
TO: PROTECTED CHARGING
Voltage, current, heat watched together
Relay cuts the charging path on a fault
LED, buzzer and LCD show the state
WHY SAFE CHARGING CHIP?
“When charging goes wrong, a battery can overheat and catch fire before anyone notices.”
THE PROBLEM
A faulty adapter, damaged cable or hot spot can push a lithium-ion cell toward thermal runaway, and phones rely on a single internal protection circuit.
OUR SOLUTION
Safe Charging Chip sits between charger and phone. An ESP32 senses voltage, current and temperature; a PYNQ-Z2 FPGA decides SAFE, WARNING or FAULT and opens the relay to cut charging.
Notes: Problem: charging faults (bad adapter, damaged cable, heat) can lead to thermal runaway, and protection is usually one internal circuit. Solution: an independent safety layer between charger and phone.

## Slide 3: TECHNICAL APPROACH
01
SENSORS
Voltage module, ACS712-5A current sensor, DS18B20
02
ESP32 EDGE NODE
12-bit ADC sampling, LCD display, UART frame out
03
FPGA SAFETY ENGINE
PYNQ-Z2 parses data and runs the safety FSM
04
PROTECTION OUTPUT
Relay cut-off, status LEDs and buzzer
IMPLEMENTATION FLOW
01
SENSE
Measure voltage, current and temperature
02
SEND
ESP32 streams readings over UART
03
DECIDE
FPGA picks SAFE, WARNING or FAULT
04
PROTECT
Relay opens, red LED and buzzer on
05
RECOVER
Reset once readings are safe
TECH STACK
PROCESSING
ESP32 and PYNQ-Z2 (Zynq-7000 FPGA)
SENSING
ACS712-5A, DS18B20, 0-25 V voltage module
COMMUNICATION
UART, 115200 baud, 8N1
ACTUATION
5 V relay, 16x2 LCD, LEDs, buzzer
SOFTWARE
Arduino C++ firmware, Verilog in Vivado
Notes: Walk the four blocks left to right, then the five-step flow. Be clear that the ESP32 stage is built and tested with potentiometers; FPGA integration is the next stage. Do not quote a measured cut-off time unless measured.

## Slide 4: FEASIBILITY & VIABILITY
DEPLOYMENT FEASIBILITY
Why it can be built
LOW-COST BUILD
Off-the-shelf ESP32, sensors and relay; the Verilog logic can later move to a CPLD or ASIC.
SAFE TO DEMONSTRATE
Potentiometers simulate faults on a dummy load, so no real battery is stressed.
REAL WORLD ISSUES
What could go wrong
SENSOR DRIFT OR FAILURE
A disconnected or inaccurate sensor can hide a real hazard.
LINK OR POWER LOSS
Lost data or supply must never leave charging switched on.
ENGINEERING SAFEGUARDS
How it stays safe
FAIL-SAFE RELAY
Normally-Open contacts open when power or the control signal is lost.
LIMITS PLUS TRENDS
Fixed limits and rate-of-change checks; watchdog and latch are planned.
Safe Charging Chip adds an independent, hardware-level cut-off to phone charging. Current status: ESP32 stage verified; FPGA integration next.
Notes: Feasibility: low-cost parts and bench-safe testing. Real-world issues: sensor failure and link or power loss. Safeguards: NO relay, limit and trend checks. Watchdog and latch are planned, not yet implemented. All testing is low-voltage DC on a dummy load.

## Slide 5: IMPACT AND BENEFITS
IMPACT ON AUDIENCE
BENEFITS OF THE SOLUTION
PHONE USERS
Early warning → Time to unplug
Independent cut-off → Protection beyond the phone
SAFETY
Independent cut-off → No single point of failure
Fail-safe relay → Power loss opens the circuit
CHARGER MAKERS & OPERATORS
Added safeguard → Higher user trust
Low-cost parts → Practical add-on
DETECTION
Voltage + current + temperature → Fuller picture
Trend checks → Earlier warning
HOMES & PUBLIC SPACES
Shared charging points → Safer use
Overnight charging → Lower fire risk
DESIGN
Verilog logic → Path to CPLD or ASIC
Modular stages → Test each on its own
MONITOR • DECIDE • PROTECT
Notes: Impact on phone users, charger makers and operators, and homes and public spaces. Benefits: independent safety, fuller detection, and a design path toward a compact chip. Avoid quoting numbers you have not measured.

## Slide 6: RESEARCH & REFERENCES
1. Project Documentation
LogicNova project synopsis
Safe Charging Chip for Mobile Phones
ESP32 adapter safety prototype
Wiring guide and pin map
Presentation and viva guide
Verified vs planned status
2. Platforms & Tools
PYNQ framework (PYNQ-Z2)
FPGA board and Jupyter overlay flow — pynq.io
AMD Vivado and Zynq-7000
Verilog design, simulation and bitstream — amd.com
3. Technical Components
Espressif Systems
ESP32 — Wi-Fi and Bluetooth MCU with 12-bit ADC — docs.espressif.com
Allegro MicroSystems
ACS712-5A Hall-effect current sensor — allegromicro.com
Analog Devices (Maxim)
DS18B20 1-Wire digital temperature sensor — analog.com
Low-voltage test rule
Isolated low-voltage DC and a dummy load only; never mains or a real phone battery
Notes: References are component documentation and your own project documents. Add any battery-safety papers or standards you want to cite once you have confirmed the exact sources.